## Slide 1: Space Gravitational-wave observatory: DECIGO
Original
Picture : Sora
On behalf of
DECIGO working group
Masaki Ando
(National Astronomical Observatory of Japan)

## Slide 2: DECIGO Working Group
Koh-suke Aoyanagi, Kazuhiro Agatsuma, Hideki Asada, Yoichi Aso, Koji Arai, Akito Araya, Masaki Ando, Kunihito, Ioka, Takeshi Ikegami, Takehiko Ishikawa, Hideharu Ishizaki, Hideki Ishihara, Kiwamu Izumi, Kiyotomo Ichiki, Hiroyuki Ito, Yousuke Itoh, Kaiki T. Inoue, Akitoshi Ueda, Ken-ichi Ueda, Masayoshi Utashima, Yumiko Ejiri, Motohiro Enoki, Toshikazu Ebisuzaki, Yoshiharu Eriguchi, Naoko Ohishi, Masashi Ohkawa, Masatake Ohashi, Kenichi Oohara, Yoshiyuki Obuchi, Kenshi Okada, Norio Okada, Nobuki Kawashima, Fumiko Kawazoe, Isao Kawano, Seiji Kawamura, Nobuyuki Kanda, Kenta Kiuchi, Naoko Kishimoto, Hitoshi Kuninaka, Hiroo Kunimori, Kazuaki Kuroda, Hiroyuki Koizumi, Feng-Lei Hong, Kazunori Kohri, Wataru Kokuyama, Keiko Kokeyama, Yoshihide Kozai, Yasufumi Kojima, Kei Kotake, Shiho Kobayashi, Motoyuki Saijo, Ryo Saito, Shin-ichiro Sakai, Masaaki Sakagami, Shihori Sakata, Norichika Sago, Misao Sasaki, Shuichi Sato, Takashi Sato, Masaru Shibata, Hisaaki Shinkai, Naoshi Sugiyama, Rieko Suzuki, Yudai Suwa, Naoki Seto, Kentaro Somiya, Hajime Sotani, Takeshi Takashima, Tadashi Takano, Kakeru Takahashi, Keitaro Takahashi, Tadayuki Takahashi, Hirotaka Takahashi, Fuminobu Takahashi, Ryuichi Takahashi, Ryutaro Takahashi, Takamori Akiteru, Hideyuki Tagoshi, Hiroyuki Tashiro, Takahiro Tanaka, Keisuke Taniguchi, Atsushi Taruya, Takeshi Chiba, Shinji Tsujikawa, Yoshiki Tsunesada, Kimio Tsubono, Morio Toyoshima, Yasuo Torii, Kenichi Nakao, Kazuhiro Nakazawa, Shinichi Nakasuka, Hiroyuki Nakano, Shigeo Nagano, Kouji Nakamura, Takashi Nakamura, Yoshinori Nakayama, Atsushi Nishizawa, Erina Nishida, Kazutaka Nishiyama, Yoshito Niwa, Kenji Numata, Taiga Noumi, Tatsuaki Hashimoto, Kazuhiro Hayama, Tomohiro Harada, Wataru Hikida, Yoshiaki Himemoto, Hisashi Hirabayashi, Takashi Hiramatsu, Mitsuhiro Fukushima, Ryuichi Fujita, Masa-Katsu Fujimoto, Toshifumi Futamase, Ikkoh Funaki, Mizuhiko Hosokawa, Hideyuki Horisawa, Kei-ichi Maeda, Hideo Matsuhara, Osamu Miyakawa, Umpei Miyamoto, Shinji Miyoki, Shinji Mukohyama, Mitsuru Musha, Toshiyuki Morisawa, Mutsuko Y. Morimoto, Shigenori Moriwaki, Kent Yagi, Hiroshi Yamakawa, Toshitaka Yamazaki, Kazuhiro Yamamoto, Chul-Moon Yoo, Jun'ichi Yokoyama, Shijun Yoshida, Taizoh Yoshino, Yaka Wakabayashi, Tomotada Akutsu, Nobuyuki Matsumoto, Ayaka Shoda, Yuta Michimura, Nobuyuki Tanaka, Sachiko Kuroyanagi, Dan Chen, Satoshi Eguchi, Rina Gondo, Kazunori Shibata, Takafumi Ushiba,

## Slide 3
    ・ DECIGO
    ・ DECIGO Pathfinder
    ・ SWIM
Notes: This talk contains two parts.
The first part is for DECIGO. I will present overview, science , and conceptual design of DECIGO.
The second part is for DECIGO pathfinder, which is the first milestone mission for DECIGO.
In this part, I will present overview, science, and current status of DECIGO pathfinder.

## Slide 4
DECIGO

## Slide 5: DECIGO
DECIGO
Space GW antenna (~2027)
Obs. band around 0.1 Hz
Terrestrial Detectors
(Ad. LIGO, KAGRA, etc)
DECIGO
LISA
(Deci-hertz interferometer Gravitational wave Observatory)
‘Bridge’ the obs.gap between
LISA and Terrestrial detectors
Notes: The first topic is sciences of DECIGO.
DECIGO stands for Deci-hertz....., firstly proposed in 2001.
This is a space GW antenna with observation band around 0.1Hz.
Since this frequency band is between the terrestrial detectors and LISA,
DECIGO will bridge the observation gap between them.

## Slide 6: DECIGO Interferometer
Interferometer Unit:
Differential FP interferometer
Laser
Photo-
detector
1000km
Arm cavity
Drag-free S/C
Arm cavity
Mirror
Baseline length: 1000 km
3 S/C formation flight
3 FP interferometers
Drag-free control
Notes: DECIGO will be formed by three spacecraft, 1000km apart from one another.
Each spacecraft has test-mass mirrors inside it, and the distances between
them are measured by means of laser interferometers.

## Slide 7: Targets and Science
DECIGO
(1 unit)
IMBH inspiral (z~1)
Merger
Frequency [Hz]
GW amplitude [Hz-1/2]
10-4
10-2
100
102
104
10-24
10-22
10-20
10-18
10-16
10-26
DECIGO
(Correlation)
Background GW
(Ωgw ~ 2 x 10-15)
NS inspiral (z~1)
Merger
3month
IMBH binary inspiral
NS binary inspiral
Stochastic background
Galaxy formation (Massive BH)
Cosmology (Inflation, Dark energy)
Fundamental physics
Notes: With this configuration, DECIGO will have this sensitivity curve.
The horizontal axis is frequency, and the vertical axis is sensitivity to GWs in unit of per-root-hertz.
DECIGO has three main targets.
The first one is inspiral of intermediate-mass BHs.
This line represents the amplitude of signal from 1000 solar mass blackhole
binaries at the distance of redshift of one. The binary will merge at the center of the DECIGO band.
This observation may bring us information on the formation of supermassive BHs at the center of galaxies.
The second target is inspiral of neutron star binaries. This yellow line shows
the GW signal amplitude for NS binary at distance of redshift one. The signal is
in the DECIGO band about several years before the merger. The signal moves to higher
frequency in time, and the merger signal will radiated in the band of ground-based
detectors. So DECIGO will work as a predictor for ground based detectors.
The third target is stochastic background GWs from the early universe.
For this target, we need multiple detectors, in order to distinguish the signal
from detectors noise, This green curve represents the noise level by one-year
cross-correlation observation with two interferometer units.
This level reaches to gravitational-wave energy density ratio of 2 times 10^-16.

## Slide 8: Astronomy and Cosmology
・Verification of the alternative theories of gravity
Test Brans-Dicke theory by NS/BH binary evolution
 Stronger constraint by 104 times
K. Yagi and T. Tanaka, Prog. Theor. Phys. 123, 1069 (2010)
・ Neutron-star physics
Determine masses of 105 NSs per year
 Constrain the EoS of NS
Formation process of NS from the spectrum
・ Black hole dark matter
Gravitational collapse of the primordial density fluctuations
 Primordial black holes (PBHs)
as a candidate of dark matter
R. Saito and J. Yokoyama, Phys. Rev. Lett. 102 161101 (2009)

## Slide 9: Characterization of inflation
Stochastic
Background GWs
Direct probe to
the history of the Universe
35
Notes: As for the stochastic background gravitational waves, DECIGO has a potential to see
directory the very beginning of the universe. The picture of the earliest universe we have
is obtained from cosmic microwave background. This is a picture of 0.4 million years after the
beginning of the universe. There are several proposals to observe the first stars and first galaxies
using infrared and optical telescopes. These targets were formed about hundred millions to billion
years after the beginning of the universe. Using gravitational waves, DECIGO would watch the
very beginning, less than one seconds from the beginning of the universe.

## Slide 10: Pre-Conceptual Design
Interferometer Unit:
Differential FP interferometer
Laser
Photo-
detector
Arm cavity
Drag-free S/C
Arm cavity
Mirror
Arm length: 1000 km
Finesse: 10
Mirror diameter: 1 m
Mirror mass: 100 kg
Laser power: 10 W
Laser wavelength： 532 nm
S/C: drag free
3 interferometers
Notes: Next, I will talk on the pre-conceptual design of DECIGO.
One interferometer unit is formed by three spacecraft.
Each spacecraft has test-mass mirrors inside it.
A mirror has a diameter of 1m and weight of 100kg.
These mirrors forms Fabry-Perot interferometers with a finesse of 10 and a baseline length of 1000km.
As light sources, we will use green lasers with output power of 10W.
So as to suppress the effect of external disturbances on test mass mirrors,
such as solar radiations, each spacecraft is drag-free-controlled.
I mean, the position of spacecraft is controlled to follow the test mass position.

## Slide 11: Interferometer Design
Transponder type vs Direct-reflection type
WD-WD
confusion noise
Decisive factor: Binary confusion noise
Compare : Sensitivity curves and Expected Sciences
Notes: One of the key features of DECIGO is to use Fabry-Perot cavities for the baseline
length change measurement. Since DECIGO has between the observation band of LISA and
ground-based detectors, we have two choices in the selection of interferometer configuration.
One choice is to adopt optical transponder-type interferometer and shorten the
baseline from LISA. The estimated noise level is shown by this orange curve.
Another choice is to adopt Fabry-Perot interferometer as ground based detectors,
and expand the baseline. The noise level with this configuration is shown
by this red curve. Optical-transponder type has advantage in low frequencies,
because it can have longer baselines, and the acceleration noises on the
test mass can be relatively suppressed. The Fabry-Perot type has an advantage in
high-frequency band and best floor sensitivity. This is because the laser power
is effectively accumulated in the cavities, and the shot noise level can be suppressed.

## Slide 12: Arm length
Cavity arm length : Limited by diffraction loss
Effective reflectivity (TEM00  TEM00)
Laser wavelength : 532nm
Mirror diameter: 1m
Optimal beam size
1000 km
is almost max.

## Slide 13: Cavity and S/C control
Local Sensor
Actuator
Displacement signal between the two Mirrors
Thruster
Thruster
Displacement Signal between S/C and Mirror
Mirror
S/C 1
S/C 2
Fig: S. Kawamura
Cavity length change
PDH error signal  Mirror position (and Laser frequency)
Relative motion between mirror and S/C
Local sensor  S/C thruster
Notes: Here, I will talk a little more on the compatibility of Fabry-Perot cavity length
control and drag-free control of the space craft position.
This figure shows one arm cavity of DECIGO.
The distance between the mirrors is measured by Fabry-Perot cavity. The signal
is fed back to the mirror position to keep the cavity length, using mirror actuators.
On the other hand, relative displacement between a mirror and S/C are measured by
local sensors around the mirrors, These signals are fed back to the thrusters attached
to the S/C. In short, this mirror follows the motion of this mirror, and each S/C
follows the mirror inside it. So, cavity control and drag-free controls are compatible.

## Slide 14: Requirements
Sensor Noise
Shot noise 3 x 10-18 m/Hz1/2 (0.1 Hz)
Acceleration Noise
Force noise 4x10-17 N/Hz1/2 (0.1 Hz)
Other noises should be well below the shot noise
Laser freq. noise: 1 Hz/Hz1/2 (1Hz)
Stab. Gain 105, CMRR 105
x 10 of KAGRA in phase noise
x 1/50 of LISA
External force sources
Fluctuation of magnetic field, electric field,
gravitational field, temperature, pressure, etc.
Notes: This viewgraph shows important requirements to reach the target sensitivity of DECIGO.
For displacement noise, 3x10^-18 m/sqrt of Hz is requires at the frequency band of 0.1Hz.
This level is about 10 times easer than that of ground based detectors.
For laser frequency noise, 1 Hz/sqrt Hz is requires for laser source,
and 10^5 gain is required for stabilization by arm cavities assuming 10^5 CMRR.
As for the acceleration noise, 4x10^-17 N/Hz^1/2 is required. This is 50 times
stringent requirement than LISA. This will be one of the most challenging requirement
in DECIGO. To realize this, we have to deeply investigate various kinds of noise sources.

## Slide 15: Orbit and Constellation
Record-disk orbit around the Sun
Relative acc. 4x10-12 m/s2
(Mirror force ~10-9 N )
Separated
unit
Constellation
4 interferometer units
2 overlapped units  Cross correlation
2 separated units  Angular resolution
overlapped
units
Separated
unit
Candidate of orbit:
Notes: The selection of orbit is a critical issue to suppress the effect of external force noise.
The obit of DECIGO is not decided yet. But the strongest candidate is a record disk
orbit along the Earth orbit around the sun as LISA. With this orbit, the relative acceleration
between test masses will be 4x10-12 m/s^2.
This acceleration corresponds to a force range of 10^-9 N for mirror actuator.
Another candidate is a halo orbit around a Lagrange point between the earth and the sun.
This is known to be a stable orbit. However, The relative acceleration is estimated
to be 4x10^-7 m/s^2, which requires larger actuation force to mirrors by 5 orders.
Thus, we adopted the record-disk orbit in the current pre-conceptual design.
As for the constellation, DECIGO will consist of 4 interferometer units.
Two of them will be placed in an overlapped place. This is required to take cross-correlation
of multiple detectors, and to distinguish the stochastic background signal from detector noises.
The other two units will be arranged at separated point along the same orbit.
These units enables us to increase angular resolution for the sky position of the source.
These are required to identify the sources and determine their redshift parameter.

## Slide 16: Foreground Cleaning
DECIGO obs. band: free from WD binary foreground
 Open for cosmological observation
DECIGO will watch
~ 105 NS binaries
Foreground for GWB
Require accurate waveform
→ Δm/m < ~10-7 %
In principle, possible
to remove them.
Fig: N. Kanda

## Slide 17: Design Update
By T.Akutsu

## Slide 18: GW observation roadmap
2010
2015
2020
2025
Detection rate
~10 event/yr
Ground-based Observatory
Better sensitivity (10Hz-1kHz)
Space-borne observatory
0.1mHz-10mHz
Guaranteed sources
0.1Hz band
Cosmological GWs
Low-freq. observation (<1Hz)
KAGRA
Ａｄ. ＬＩＧＯ
LPF
DECIGO
DECIGO
LISA
BBO
LIGO
TAMA
Enhanced
LIGO
CLIO
Advanced
LIGO
KAGRA
Advanced
Virgo
Virgo
ET
LPF
DPF
Pre-DECIGO
LISA

## Slide 19: Roadmap
 | 2010 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Objective | Space test of key tech. GW observation |  |  |  |  |  |  |  | Detect GW with min. spec FP between S/C |  |  |  |  |  |  | GW astronomy |  |  |  |  | 
Design | Single small satellite Short FP interferometer |  |  |  |  |  |  |  | 3 S/C 1 interferometer unit |  |  |  |  |  |  | 3 S/C x 3-4 units |  |  |  |  | 
Figure: S.Kawamura
DECIGO
Pathfinder
(DPF)
Pre-DECIGO
DECIGO
R&D
Fabrication
R&D
Fabrication
R&D
Fabrication
SDS-1/SWIM

## Slide 20
DECIGO Pathfinder

## Slide 21: DECIGO-PF
DECIGO Pathfinder (DPF)
Single satellite
(Payload ~1m3 , 350kg)
Low-earth orbit
(Altitude 500km, sun synchronous)
30cm FP cavity with 2 test masses
Stabilized laser source
Drag-free control
First milestone mission for DECIGO
Shrink arm cavity
DECIGO 1000km  DPF 30cm
DECIGO
1000km
Local Sensor
Actuator
Thruster
Laser
DPF
30cm
Notes: Here, I will go on to the second part of my talk, on the DECIGO pathfinder.
DPF is the first milestone mission for DECIGO. The original purpose is to test the
key technologies for DECIGO. For this purpose, DPF is designed to be a prototype
of DECIGO. In DPF, one 1000km arm of DECIGO is shrunk down to 30cm, and placed
inside one small satellite orbiting around the earth.
A 30cm Fabry-Perot cavity is formed by two test mass mirrors. And the length change
is measured by means of stabilized laser. The relative displacement between the test
mass and the satellite is measured by a local sensor, and the signals are fed back to the
satellite thrusters to realize drag-free control.

## Slide 22: DPF satellite
Stabilized.
Laser source
Interferometer
module
Satellite
Bus system
Solar Paddle
Mission
Thruster head
On-board
Computer
Bus thruster
Satellite Bus
(‘Standard bus’ system)
DPF Payload
Size : 950mm cube
Weight : 150kg
Power : 130W
Data Rate: 800kbps
Mission thruster x12
Power Supply
SpW Comm.
Size :
950x950x1100mm
Weight : 200kg
SAP : 960W
Battery: 50AH
Downlink : 2Mpbs
DR: 1GByte
3N Thrusters x 4
Notes: DPF satellite will look like this figure. The satellite is comprised of two parts.
The bottom part contains the bus system with solar puddles, batteries, data processing system,
temperature control system, and telecommunication system with ground station.
The upper part is a mission payload. The interferometer module is placed in the first floor,
and stabilized laser system is placed in the second floor. 10 small low-noise thrusters
are attached at the corners of the payload.

## Slide 23: DPF mission payload
Fabry-Perot interferometer
Finesse : 100
Length : 30cm
Test mass : ~a few kg
Signal extraction by PDH
Drag-free control
Local sensor signal
 Feedback to thrusters
Mission weight : ~150kg
Mission space : ~95 x 95 x 90 cm
Laser source
Yb:YAG laser (1030nm)
Power : 25mW
Freq. stab. by Iodine abs. line
Thruster
Notes: This figure show the design of mission payload part.
As a laser source, we will use a Yb:YAG laser stabilized using iodine absorption line.
The stabilized beam is introduced to the 30cm main interferometer,
formed by two test mass mirrors.
The length change signal is extracted by a Pound-Drever-Hall scheme. The signal is fed back
to the mirror using electro-static-type actuators. The relative displacement between the
test mass and the satellite is monitored by electro-static-type local sensors and fed back to
the mission thrusters to realize dreg-free-control.

## Slide 24: DPF Sensitivity
Satellite mass : 350kg, Area: 2m2
Altitude: 500km
Thruster noise: 0.1μN/Hz1/2
Laser source : 1030nm, 25mW
IFO length : 30cm
Finesse : 100, Mirror mass : 1kg
Q-factor : 105, Substrate: TBD
Temperature : 293K
(Preliminary parameters)
Notes: With this configuration, DPF will have this sensitivity curve. The black curve represents
the DPF sensitivity to GW signals. This level is mainly limited by laser frequency noise
in high frequency band, and acceleration noise in low frequency band.

## Slide 25: Targets of DPF
Scientific observations
Gravitational Waves form BH mergers
 BH formation mechanism
Gravity of the Earth
 Geophysics, Earth environment
Science technology
Space demonstration for DECIGO
 Most tech. with single satellite
(IFO, Laser, Drag-free)
Precision measurement in orbit
 IFO measurement
under stable zero-gravity

## Slide 26: DPF Science
Astronomical observation
GW from merger of IMBHs
 Formation mechanism
of supermassive BHs
~30 GCs within DPF range
NGC6441
NGC6256
NGC7078
NGC7093
NGC104
Observation of the earth
Gravitational potential
 Shape of the earth
Environment monitor
Comparable sensitivity
with other missions
Spatial
Scale
80km
100km
By A.Shoda
By K.Yagi

## Slide 27: GW target of DPF
NGC6441
NGC6256
NGC7078
NGC7093
NGC104
Observable range covers
our Galaxy (SNR~5 )
IMBH inspiral and merger
Obs. Duration (~1000sec)
Obs. Distance 40kpc,
for m = 2 x104 Msun
KAGAYA
Black hole events
in our galaxy
Hard to access by others
 Original observation
(By K.Yagi)
There may be IMBH at GCs
DPF covers ~30 GCs
Notes: However, DPF has scientific targets, which are blackholes in our galaxy.
Inspiral and coalescence of intermediate-mass blackhole is one of the main targets of DECIGO,
and also a main target of DPF. This figure shows the observable range of DPF as a function
of blackhole mass.
The green curve is the range for BH inspirals, and this green curve is for quasi-normal modes.
This red line represents the distance to the galactic center. So this figure shows that
DPF has sufficient sensitivity to observe events at the center of our galaxy, if any.
Since this frequency band, around 0.1Hz, is hard to access by ground-based detectors,
this will be an original observation.

## Slide 28: Earth’s Gravity Observation
Measure gravity field of the Earth
from Satellite Orbits, and gravity-gradiometer
Determine global gravity field
 Basis of the shape of
the Earth (Geoid)
Monitor of change in time
 Result of Earth’s dynamics
Ground water motion
Strains in crusts by
earthquakes and volcanoes
Seasonal change of the gravitational potential observed by GRACE
comprehensive and homogeneous-quality data

## Slide 29: Satellite Gravity missions
Satellite-to Satellite
tracking High-Low
Satellite-to Satellite
tracking Low-Low
Satellite
Gravity Gradiometry
・Observe satellite orbit
by global positioning
system (GPS,…)
・Cancel drag-effects
by accelerometer
・Distance meas. by
along-track satellites
・Cancel drag-effects
by accelerometer
・Observe potential by
gravity gradiometer
・Drag-free control for
cancellation of drags
GRACE (NASA, 2002-)
CHAMP (GFZ, 2000-)
GOCE (ESA, 2009-)
3-types of satellite gravity missions

## Slide 30: DPF sensitivity
Report for Mission Selection
Gravity Field and Steady-State
Ocean Circulation Mission
ESA SP-1233(1) July 1999.
400km
Scale
80km
100km
(with margin 10)
Better in low orders (large scale)  Sensors
Worse in high orders (small scale)  Altitude
Comparison of sensitivities

## Slide 31: DPF mission status
1st mission (2012): SPRINT-A/EXCEED
2nd mission (~2015) : SPRINT-B/ERG
3rd mission (~2016/17) : TBD
Call for proposal : 2012
DPF : One of the candidate of
JAXA’s small satellite series
At least 3 satellite in 5 years with
Standard Bus + M-V follow-on rocket
DPF survived until final two
SPRINT-A /EXCEED
UV telescope mission
Next-generation
Solid rocket booster (M-V FO)
Fig. by JAXA
DPF is one of the strongest
candidates of the 3rd mission
Notes: Now, I will talk on the current status of the mission selection.
JAXA, the Japanese space agency, has a project to launch at least three small satellites
in five years, using a standard bus system and a next generation solid rocket booster.
At the beginning, there were about fifty proposals four years ago. And fifteen missions
were accepted as official working groups three years ago.
Among them about five missions has been financially supported by JAXA since two years ago.
The first mission has already decided to be a SPRINT-A/EXCEED mission, which is a UV
telescope mission for planetary science. The second mission is now in selection.
DPF is surviving as one of the two final candidates. Another candidate is named ERG,
which is for observation of magnetic fields around the earth during active years of the Sun.
The final hearing was held last month, and the final selection will be made in this month.

## Slide 32: DPF-WG activities
Mission design
・Structure and thermal modeling
・Drag-free control design
Design : NEC

## Slide 33: DPF-WG activities
Interferometer module
BBMs (Bread-board model) for Core components
UEC, NICT, NASA/GSFC
Test-mass module
Laser stabilization module
Univ. of Tokyo,NAOJ
Low-noise thruster module
JAXA
NAOJ, Hosei Univ.

## Slide 34
SWIM

## Slide 35: Roadmap
 | 2010 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Objective | Space test of key tech. GW observation |  |  |  |  |  |  |  | Detect GW with min. spec FP between S/C |  |  |  |  |  |  | GW astronomy |  |  |  |  | 
Design | Single small satellite Short FP interferometer |  |  |  |  |  |  |  | 3 S/C 1 interferometer unit |  |  |  |  |  |  | 3 S/C x 3-4 units |  |  |  |  | 
Figure: S.Kawamura
DECIGO
Pathfinder
(DPF)
Pre-DECIGO
DECIGO
R&D
Fabrication
R&D
Fabrication
R&D
Fabrication
SDS-1/SWIM

## Slide 36: Rotating TOBA : SWIMmn
Test mass
Photo sensor
Coil
TAM: Torsion Antenna Module with free-falling test mass
(Size : 80mm cube, Weight : ~500g)
Reflective-type optical
displacement sensor
Separation to mass ~1mm
Sensitivity ~ 10-9 m/Hz1/2
6 PSs to monitor mass motion
~47g Aluminum, Surface polished
Small magnets for position control
Spin Axis
(46.5mHz)
80mm
Small Module SWIMmn on SDS-1
Photo：
JAXA
Launched Jan. 2009, Terminated Sept. 2010

## Slide 37: Sensitivity
Though limited by non-fundamental noises,
best as a space-borne GW detector.
By W.Kokuyama

## Slide 38: Observation by SWIM
Continuous data taking
Orbital Period
10mHz LPF
Jun 17, 2010 ~120 min.
July 15, 2010 ~240 min.
Tokyo
Kyoto
Orbital period
~100min.
Observation band
By W.Kokuyama

## Slide 39: Upper Limit on GWB
Upper Limit at two frequencies (two polarizations)
(C.L. 95%, f0 18mHz, BW 4mHz)
By W.Kokuyama
‘Forward’ mode
‘Reverse’ mode

## Slide 40
Summary

## Slide 41: Summary
DECIGO : Fruitful Sciences
Very beginning of the Universe
Dark energy, Dark matter
Galaxy formation
DECIGO Pathfinder
Important milestone for DECIGO
Observation of GWs and Earth’s gravity
Strong candidate of JAXA’s satellite series
SWIM – Operation in orbit
first precursor to space!
Notes: Now, I will summarize my talk.
DECIGO will provide us fruitful knowledge on the beginning of the universe, dark energy,
and formation of galaxies.
DECIGO pathfinder is a first milestone mission for DECIGO, and being a
strong candidates of JAXA's small satellite series.
In addition, we have developed a SWIM module, which is under operation in orbit.
This is our first precursor to space. Though this is only a small module, we have made
a significant step

## Slide 42: Collaboration and support
・Supports from LISA
Technical advices from LISA/LPF experiences
Support Letter for DECIGO/DPF, Joint workshop (2008.11)
・Collab. with Stanford univ. group
Drag-free control of DECIGO/DPF
UV LED Charge Management System for DPF
・Collab. with NASA/GSFC
Fiber Laser , Earth’s gravity observation
・Collab. with JAXA Trajectory and Navigation group
 Formation flight of DECIGO, DPF drag-free control
・Geophysics group (Kyoto, ERI, UEC, NAOJ)
・Advanced technology center ( ATC) of NAOJ
・JAXA’s fund for small satellite development
・Research Center for the Early Universe (RESCEU), Univ. of Tokyo
Notes: In addition to this organization, we have collaboration with and supports from other groups.
The LISA/LPF group members are providing us technical advises from their experiences.
In the last autumn, we had the 1st LISA-DECIGO joint workshop at JAXA, Japanese space agency.
This workshop was also helpful for us in political point of view. The JAXA peoples were
really impressed in the success of this workshop and the supports from LISA group.

## Slide 43
    End
Original
Picture : Sora
Notes: Thanks you for your attention.

## Slide 44: Organization
Detector
Sato (Hosei)
Akutsu (NAOJ)
Ueda (NAOJ)
Aso (Tokyo)
PI: Kawamura (NAOJ)
Deputy: Ando (Kyoto)
Executive Committee
Kawamura (NAOJ), Ando (Kyoto), Seto (Kyoto), Nakamura (Kyoto), Tsubono (Tokyo), Tanaka (Kyoto), Funaki (ISAS), Numata (Maryland), Sato (Hosei), Kanda (Osaka city), Takashima (ISAS), Ioka (KEK), Yokoyama (Tokyo)
Pre-DECIGO
Sato (Hosei)
Satellite
Funaki (ISAS)
Science, Data
Tanaka (Kyoto)
Seto (Kyoto)
Kanda (Osaka city)
DECIGO pathfinder
Leader: Ando (Kyoto)
Laser
Musha (ILS)
Ueda (ILS)
Drag free
Sato (Hosei)
Thruster
Funaki (ISAS)
Bus
Takashima (ISAS)
Data
Kanda (Osaka city)
Detector
Akutsu (NAOJ)
Numata (Maryland)
Mission phase
Design phase
Notes: This shows the organization of DECIGO. The leader is Seiji Kawamura.
The upper part is organized as a design team for DECIGO. The organization also includes
a DECIGO pathfinder working group, shown in the lower part. This part is organized
as a mission phase team, and the subgroups are in charge of research and development tasks.

## Slide 45
Supplementary topic

## Slide 46: KAGRA and DECIGO
KAGRA (~2016)
Terrestrial Detector
 High frequency events
Target: GW detection
DECIGO (~2027)
Space observatory
 Low frequency sources
Target: GW astronomy

## Slide 47: Roadmap
 | 2010 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Objective | Space test of key tech. GW observation |  |  |  |  |  |  |  | Detect GW with min. spec FP between S/C |  |  |  |  |  |  | GW astronomy |  |  |  |  | 
Design | Single small satellite Short FP interferometer |  |  |  |  |  |  |  | 3 S/C 1 interferometer unit |  |  |  |  |  |  | 3 S/C x 3-4 units |  |  |  |  | 
Figure: S.Kawamura
DECIGO
Pathfinder
(DPF)
Pre-DECIGO
DECIGO
R&D
Fabrication
R&D
Fabrication
R&D
Fabrication
SDS-1/SWIM
Notes: As shown in the previous viewgraph, DECIGO requires huge resources. So, we have a roadmap
to realize it step by step. We are planning to launch two milestone missions.
The first one is named DECIGO pathfinder, or DPF in short. This is a single satellite
orbiting around the earth. The purpose of DPF is to test the key technologies for DECIGO,
and also to carry out observation runs. The second milestone mission is named pre-DECIGO.
This will consist of three spacecraft. The purpose of pre-DECIGO is to detect GWs with
minimum interferometer specifications.

## Slide 48
Introduction

## Slide 49: Expanding the Horizon
First-gen. GW detectors : ~ 20Mpc obs. range
However… we can expect only rare events
(10-4-10-2 event/yr)
Next generation detectors
Better sensitivity
to cover more galaxies
Wider observation band
for various sources
DECIGO
LCGT
Core-collapse
Supernovae
NS binary
inspiral
ScoX-1
(1yr)
Pulsar
(1yr)
Massive BH
inspirals
Galaxy
binaries
Gravity-gradient noise
(Terrestrial detectors)
DPF limit
Background GWs
from early universe
(Wgw=10-14)
Foreground GWs
LISA

## Slide 50: Expanding the observation band
GW frequency ~ 1/ (time scale of the source)
Observation at low frequency
- Larger-mass events  larger amplitude GW
- (Almost) stationary source  Do not have to wait for ‘events’
Different or complementary science
(Example) GW from compact binary inspiral
Separation
Mass
- Large separation
 stationary, low-freq. GWs
- Just before merger ( )
 Large mass, large amplitude GWs at low freq.

## Slide 51: Sources and detectors
DECIGO
LCGT
Core-collapse
Supernovae
NS binary
inspiral
ScoX-1
(1yr)
Pulsar
(1yr)
Massive BH
inspirals
Galactic
binaries
Gravity-gradient noise
(Terrestrial detectors)
Background GWs
from early universe
(Wgw=10-14)
Foreground GWs
LISA
Ground-based detectors : 10Hz - 1kHz  Neutron star, Supernova, …
DECIGO/BBO : 0.1 - 1Hz  IMBH, Background GWs, …
LISA : 1mHz – 0.1Hz  SMBH, Compact binary,...
Notes: DPF has almost the same observation band with that of DECIGO. But the floor level is worse by 8 orders.

## Slide 52: Space GW detector
- Longer baseline
Observation freq. band
∝ 1 / (Beam storage time) ∝ Baseline length
Suppression of displacement noise
Strain sensitivity ~ (disp. noise) / (Baseline length)
Advantages of a space detector for low-freq. observation
- Free from noises by the earth
Seismic noise, gravity-gradient noise
Disadvantages of a space detector
- Cost, Development time
- Maintenance and upgrade are almost impossible after launch

## Slide 53: Space-borne observatories
LISA (Laser Interferometer Space Antenna)
Obs. band around 1mHz
~Million km baseline length
Recent change : ESA/NASA  ESA mission
Design updates underway
 changing name to
NGO (New Gravitational-wave Observatory)
DECIGO
(Deci-hertz Interferometer
Gravitational Wave Observatory)
Obs. Band around 0.1Hz
1000km baseline length
Laser
Photo-
detector
Arm cavity
Drag-free S/C
Arm cavity
Mirror

## Slide 54: NGO (LISA) Interferometry
LISA assessment study report (Yellow Book), ESA/SRE (2011) 3, February 2011
LISA web page : http://sci.esa.int/lisa
Interferometer design
- Optical transponder configuration
Long baseline (~1 million km) power loss by diffraction
Each S/C has laser source Phase-lock to incoming beam

## Slide 55: LISA Pathfinder
M Hewitson for the LPF team, AMALDI, July 15th 2011
LISA Pathfinder
- Technical test for LISA
Obtain the best geodesic motion possible
Differential acceleration of the two TMs
3 x 10-14 m s-2 at 1 mHz
Determine best configuration by experiments
Develop a noise model of the system
Allows the projection of the performance of
technologies to LISA
- Status
Most of the hardware is there.
Awaiting thrusters and launch lock.
Most of the experiments
are already defined.
- Launch in 2014

## Slide 56: Dark energy
DECIGO will observe
5x104 NS binaries for z<1
Precise ‘clock’ at cosmological distance
Angular resolution
～10arcmin2 （1 detector）
～10arcsec2 （3 detectors）
at z=1
Determine cosmological parameters
Absolute and independent measurement
 Information on acceleration
of expansion of the universe
chirp waveform
Distance:
Redshift:
host galaxy
‘Standard Siren’
Relationship between
distance and redshift
NS-NS (z～1)
GW
DECIGO
Output
Expansion ＋Acceleration?
Seto, Kawamura, Nakamura,
PRL 87, 221103 (2001)
Notes: I will talk a little more on the sciences form the NS binaries and stochastic background.
For Newton-star binaries, DECIGO is not just a predictor of merger for ground-based detectors.
DECIGO will observe 10 thousand to hundred thousand binaries at a distance of redshift of one.
This means that we have plenty of precise clocks at cosmological distance.
These clocks can be used as standard sirens. The distance to the source is directory
measured by the gravitational waveform. And the redshift is measured by EM wave counterpart
observation by identifying the source. From this distance-to-redshift measurement,
we will be able to observe the acceleration of the expansion of the universe by dark energy.

## Slide 57: Galaxy formation
戎崎俊一(理化学研究所) 先生のwebページより引用 http://atlas.riken.go.jp/~ebisu/smbh.html
DECIGO will observe
Intermediate-mass BH (IMBH)
binary merger with
SNR>103 for z~10 source
Information on the
formation of
Supermassive BHs
at the center of galaxies

## Slide 58: Roadmap
 | 2010 | 11 | 12 | 13 | 14 | 15 | 16 | 17 |  | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Objective | Space test of key tech. GW observation |  |  |  |  |  |  |  | Detect GW with min. spec FP between S/C |  |  |  |  |  |  | GW astronomy |  |  |  |  | 
Design | Single small satellite Short FP interferometer |  |  |  |  |  |  |  | 3 S/C 1 interferometer unit |  |  |  |  |  |  | 3 S/C x 3-4 units |  |  |  |  | 
Figure: S.Kawamura
DECIGO
Pathfinder
(DPF)
Pre-DECIGO
DECIGO
R&D
Fabrication
R&D
Fabrication
R&D
Fabrication
SDS-1/SWIM

## Slide 59: Interferometer Module
Interferometer Module : Test mass + IFO
NAOJ, U-Tokyo
Interferometer
Module
Interferometer
 GW, Gravity observation
Test-mass module
 Gravity reference
・30cm IFO BBM ・Packaging
Digital control ・Monolithic Opt.
Laser sensor
 Small MI
Hosei, NAOJ,
Ochanomizu, Stanford
・BBM of Module,
Sensor, Actuator,
Clump/Release
・μ-Grav. Exp.
ERI, U-Tokyo
・BBM test
・Sensitivity meas.
Notes: The prototype of the test mass mirror and the housing for it are shown in this picture.
The details of this part will be presented by S.Sato san in this afternoon in the parallel session
number two and also was presented by Yuka Wakabayashi san in a poster session.

## Slide 60: Stabilized Laser Module
Stabilized Laser : Laser source + Stabilization system
UEC, NICT
Stabilized
Laser Module
I2 absorption line
 Frequency
reference
UEC, NASA/GSFC
Yb:YAG (NPRO or Fiber laser)
 Laser source
・BBM
development
・BBM development
・Stability meas.
Notes: The laser stabilization system using iodine absorption line is being developed as BBM in
the same size as flight model. This system is working well, and evaluation of the stability
and development of automatic control system are going on.

## Slide 61: Attitude and Drag-free control
Attitude and Drag-free control : Structure, Thrusters, Control
JAXA, NDAJ, Tokai-U
Low-noise
Thruster
Low-noise Thruster
U-Tokyo, JAXA
Structure, thermal stability
Mass balance
・Passive
attitude stability
・Drag-free control
 Actuators for satellite control
・BBM and system design
Notes: The attitude and drag-free control system is being designed as shown in this figure.
DOF will have a hybrid drag-free control configuration with passive stabilization with
gravity gradient, and active control using mission thrusters.
As for the low-noise thruster, we are designing the system with existing technologies,
and developing a thruster stand used for the evaluation of thrust noises.
In addition, as a R&D for future missions, we are developing a new slit-type FEEP thruster.

## Slide 62: Signal processing and Control
Signal Processing and Control : SpaceWire-based system
Signal processor
JAXA, U-Tokyo, Kyoto
SpC2 + SpW system
 Signal processing and install. ctrl
Test-mass
control
Photo
by JAXA
SDS-1
(Jan. 2009)
SWIMmn
SpC2
SWIMmn demonstration
 Test mass control in orbit
Space demonstration
bySDS-1/SWIM
Satellite Bus
JAXA, U-Tokyo, Kyoto
Notes: As one of R&D for DPF and also DECIGO, we have made a significant step recently.
We developed a small test-mass and signal-processing module, named SWIM.
This module was loaded on a small technology demonstration satellite, and launched
in this January. We had several in-orbit operation after that, and we are obtaining
good results. In short, it is working well. Details will be presented by W.Kokuyama
in this afternoon in the parallel session number 2. I believe that this will be an
exciting talk for most of you.

## Slide 63: Gravity of the Earth
Measure gravity field of the Earth
from Satellite Orbits, and gravity-gradiometer
Determine global gravity field
 Density distribution
Monitor of change in time
Ground water motion
Strains in crusts by
earthquakes and volcanoes
GPS satellite
By Araya and Fukuda
Observation Gap
between GRACE and GRACE-FO
(2012-16)
 DPF contribution
in international network
Notes: DPF has another scientific target, which is the gravity of the earth. Changes of the global
gravity field of the earth is being monitored by several satellite missions. However,
it is said that there will be an observation gap time between the end of the GRACE mission and
the start of GRACE follow-on. DPF would be able to contribute to bridge the gap time.

## Slide 64: 地球重力場観測の観測網
GRACEとGRACE-FOの間
(2012-16年) の空白を埋める可能性
 独自の成果, 国際貢献
GRACE, GOCEが稼働中
次世代計画 GRACE-FO
GRACEと同等 (マイクロ波測距)
GRACE
L ~ 220km, ΔL ~ 5mm
 ΔL/L ~ 2 x 10-11
DPF
L ~ 0.3m, ΔL ~ 10-11 m
 ΔL/L ~ 3 x 10-11

## Slide 65: R&D for DPF (1)
Stabilized Laser
BBM development
Yb:YAG (NPRO) source
Saturated absorption by I2
 Stability test, Packaging
By M.Musha
By S.Sato
IFO and housing
BBM-EM development
 Test of concepts
+ Earth gravity sensors
By A.Araya

## Slide 66: R&D for DPF (1)
Main interferometer
BBM development
Locked with digital control
 Stability test, Packaging
By M.Michimura
By S.Sato
IFO and housing
BBM-EM development
 Test of concepts
+ Earth gravity sensors
By A.Araya

## Slide 67: R&D for DPF (2)
Attitude control and Drag-free
Satellite structure (mass distribution)
Passive attitude stabilization
by gravity gradient
Mission thruster position
Control topology
Thruster
System design
with existing tech.
Noise meas. system
(thruster stand)
Development of Slit FEEP
By I.Funaki
By
S.Moriwaki

## Slide 68: DPF and DECIGO
DECIGO
requirements
1000km FP cavity
IFO control in space
Low external force
Large optics
Ultra stable Laser
Stabilization of source
Stabilization by long arm
Formation flight
Stable orbit
Inter S/C Ranging
Drag-free control
Low-noise thruster
Observation
Data procession
Data analysis
Triggered search
DPF requirements
Satellite disp.
10-9 m/Hz1/2
Freq. Stability
0.5 Hz/Hz1/2
Disp. noise
6x10-16 m/Hz1/2
4x10-18 m/Hz1/2
Force noise
10-14 N/Hz1/2
10-17 N/Hz1/2
Thruster noise
10-7 N/Hz1/2
0.1 Hz band
Observation and
Data analysis
Precise meas.
by IFO
Stab. Laser
Drag-free
control
GW Obs.
1 Hz/Hz1/2

## Slide 69: IMBH inspiral and Merger
戎崎俊一(理化学研究所) 先生のwebページより引用 http://atlas.riken.go.jp/~ebisu/smbh.html
DECIGO will observe
Intermediate-mass BH (IMBH)
binary merger with
SNR>6000 for z~1 source
Information on the
formation of
Supermassive BHs
at the center of galaxies

## Slide 70: Standard Sources
Absolute power
or amplitude
Supernova (EM wave) Neutron-star binary (GW)
‘Standard Candle’ ‘Standard Siren’
Extrapolated from
nearby events
General Relativity
Event rate
2000/yr （SNAP）
104-5/yr （DECIGO）
Error in distance
~10%
Identification
of host galaxy
Others
Uncertainty by
dust absorption
Negligible interaction
with matters
＜
＜
＜
～
～
＞
Require multiple detectors
or statistics
R.Takahashi (2006)
10% at z=1
Easy?
Fig. from
SNAP
web page

## Slide 71: DPF targets
Credit: NASA, STScI
BHs in Globular clusters
BH masses estimated from star motion
Estimate SNR of GW signals
Equal mass, Mass ratio 1:1/3, 100Msun BH capture
(~150 Globular Clusters
in our Galaxy)
(By N.Seto)

## Slide 72: Comparison with LPF
LPF (LISA Pathfinder)
DPF (DECIGO Pathfinder)
Stabilized Laser
Interferometer
Module
Thruster
Control Unit
Solar Paddle
Interfererometer
Control Unit
Housing
Control Unit
Mission
Thrusters
Central
Processing Unit
Bus Thrusters
Purpose
Launch
Weight
Orbit
Test Mass
Laser source
Interferometer
Sensitivity
Demonstration for LISA
2010
Dedicated launcher (Vega)
1,900 kg
Halo orbit around L1
Drag-free attitude control
Au-Pt alloy x2
Nd:YAG (1064nm)
Mach-Zehnder
3x10-14 m/s2/Hz1/2 (1mHz)
Demonstration for DECIGO
GW observation
~2013
Dedicated launcher (M-V follow-on)
350 kg
SSO altitude 500km
Drag-free attitude control
TBD x2
Yb:YAG (1030nm)
Fabry-Perot
1x10-15 m/s2/Hz1/2 (0.1Hz)

## Slide 73: Pre-DECIGO
 | Pre-DECIGO | DECIGO
Arm length | 100 km | 1000 km
Mirror diameter | 30 cm | 1 m
Laser wavelength | 0.532 m | 0.532 m
Finesse | 30 | 10
Laser power | 1 W | 10 W
Mirror mass | 30 kg | 100 kg
# of interferometers in each cluster | 1 | 3
# of clusters | 1 | 4

## Slide 74: Sensitivity of Pre-DECIGO
S/N~14 for NS-NS@300Mpc, 10-20 events/year

## Slide 75: SWIM in-orbit operation
- Test of signal processing and control system
- Demonstration of space GW detector
Photo：
JAXA
CPU: HR5000
(64bit, 33MHz)
System Memory:
2MB Flash Memory
4MB Burst SRAM
4MB Asynch. SRAM
Data Recorder:
1GB SDRAM
1GB Flash Memory
SpW: 3ch
SpaceCube2: Space-qualified Computer
SWIMmn : User Module
Processor test board
GW+Acc. sensor
FPGA board
DAC 16bit x 8 ch
ADC 16bit x 4 ch
 32 ch by MPX
Torsion Antenna x2
~47g test mass
Size: 71 x 221 x 171
Weight: 1.9 kg
Power: 7W
Data Rate : 380kbps
Size: 124 x 224 x 174
Weight: 3.5 kg
Power: ~7W
Photo by JAXA
Photo by JAXA
SWIM (Space-wire Demonstration module)
on SDS-1 satellite
Launched in Jan. 23, 2009
Decommission in Sept. 2010

## Slide 76: SWIMmn
Tiny GW detector (TOBA)
Test mass bar (5cm length)
 Levitated control in space
Test mass
Photo sensor
Coil
TAM: Torsion Antenna Module with free-falling test mass
(Size : 80mm cube, Weight : ~500g)
Reflective-type optical
displacement sensor
Separation to mass ~1mm
Sensitivity ~ 10-9 m/Hz1/2
6 PSs to monitor mass motion
~47g Aluminum, Surface polished
Small magnets for position control
Used for test-mass
position control
Max current ~100mA
2 TAMs
in the frame
SWIMmn Module
See A. Shoda’s talk
on Tuesday

## Slide 77: Successful control
SWIM
In-orbit operation
z control on
yaw control on
Operation: May 12, 2009
Downlink: ~ a week
Test mass controlled
Damped oscillation
(in pitch DoF)
Error signal  zero
Signal injection
 OL trans. Fn.
Free oscillation
in x and y DoF
By
W.Kokuyama

## Slide 78: SWIMmn初期運用(5)
XY平面上のマスの動きと衛星スピンの効果
マスが浮上した時、XY平面上で自由振動を行っている様子が観測
X-Yプロット
楕円が回転
0.2mm
2Hzの共振＋うなり(~0.05Hz)
データからフィッティング：-16.8deg/s
衛星スピンレート：-16.7deg/s
スピン安定
コリオリ力により
振動軸が回転
→ 「フーコーの振り子」
Z
よく一致
X
Y
Time [sec]
Time [sec]
センサ固定座標系でみると

## Slide 79: SWIMmn初期運用(1)
浮上マスの制御
(注：データ処理のせいで
過渡応答は一部汚く見える)
そのまま地上では制御できない
(飛行機実験で20秒間の
制御を実証していた)
3回目 例：09/03/14 14時(JST)頃 ノルウェー上空
鉛直制御
回転制御
Z ON
Yaw ON
４回とも宇宙空間での
制御に成功(TAM1)
OFF
2月運用時に2回、
3月運用時に2回、
制御を実施
フォトセンサ(変位センサ)
のオフセット最適化も実施
TAM2は動作確認中

## Slide 80: SWIMmn初期運用(2)
制御時残留ノイズスペクトル
8.4Hz注入信号と3倍波
XY平面内共振(後述)と倍波
Z方向に矩形波信号注入時
その他のピーク：解析中
データの取得に成功・解析を実施中
Pitch
Rotational Displacement [rad/rHz]
10-6
10-7
10-5
10-4

## Slide 81: 球状星団のブラックホール
GEMINI AND HUBBLE SPACE TELESCOPE EVIDENCE FOR AN INTERMEDIATE-MASS
BLACK HOLE IN w CENTAURI
Eva Noyola et al., ApJ 676 (2008) 1008Y1015
中心付近の星の速度分布
と BH質量の関係
中心付近の星の速度分布の観測
Core velocity dispersions for 25 Galactic and 10 old Magellanic globular clusters?
Pierre Dubath et al.,
Astron. Astrophys. 324, 505–522 (1997)

## Slide 82: DECIGOによる初期宇宙BH観測

## Slide 83: 推進体制
DPF-WG 84名
DECIGO 137名

## Slide 84: Main interferometer
Test-mass module
Keeps a test inside
Local sensor/actuator
Launch-lock system
Interferometer sensors
for fine measurement
Fabry-Perot interferometer
Finesse : 100
Length : 30cm
Test mass : ~1kg
Signal extraction by PDH

## Slide 85: DECIGOのための根幹技術実証
DECIGOで必要
とされる主要技術
基線長1000kmのFP干渉計
宇宙における干渉計制御
試験マスに対する外乱抑圧
大型光学系の製作・制御
安定化レーザー光源による精密計測
光源の周波数・強度安定化
長基線長を利用した安定化制御
フォーメーションフライト
安定な軌道の実現
宇宙機間の距離制御
ドラッグフリー制御
低雑音スラスタ
観測運用
時系列連続データの処理
データの解析
理論予測・他の観測との比較
DPFで実証される技術
衛星変動安定度
10-9 m/Hz1/2
0.5 Hz/Hz1/2
の周波数安定度
6x10-16 m/Hz1/2
の変位感度
4x10-18 m/Hz1/2
の変位感度
10-14 N/Hz1/2
の外力雑音
10-17 N/Hz1/2
の外力雑音
スラスタ雑音
10-7 N/Hz1/2
0.1 Hz帯の連続
観測とデータ解析
宇宙干渉計
による
精密計測
安定化レーザー
の宇宙実証
ドラッグフリー
制御の実現
重力波観測

## Slide 86: DECIGOのための根幹技術実証
DECIGOで必要
とされる主要技術
基線長1000kmのFP干渉計
宇宙における干渉計制御
試験マスに対する外乱抑圧
大型光学系の製作・制御
安定化レーザー光源による精密計測
光源の周波数・強度安定化
長基線長を利用した安定化制御
フォーメーションフライト
安定な軌道の実現
宇宙機間の距離制御
ドラッグフリー制御
低雑音スラスタ
観測運用
時系列連続データの処理
データの解析
理論予測・他の観測との比較
DPFで実証される技術
衛星変動安定度
10-9 m/Hz1/2
0.5 Hz/Hz1/2
の周波数安定度
6x10-16 m/Hz1/2
の変位感度
4x10-18 m/Hz1/2
の変位感度
10-14 N/Hz1/2
の外力雑音
10-17 N/Hz1/2
の外力雑音
スラスタ雑音
10-7 N/Hz1/2
0.1 Hz帯の連続
観測とデータ解析
宇宙干渉計
による
精密計測
安定化レーザー
の宇宙実証
ドラッグフリー
制御の実現
重力波観測

## Slide 87: DPFで実証される科学技術
DPFで実証される技術
衛星変動安定度
10-9 m/Hz1/2
0.5 Hz/Hz1/2
の周波数安定度
6x10-16 m/Hz1/2
の変位感度
10-14 N/Hz1/2
の外力雑音
スラスタ雑音
10-7 N/Hz1/2
宇宙干渉計
による
精密計測
安定化レーザー
の宇宙実証
ドラッグフリー
制御の実現
意義・波及効果
宇宙空間での精密計測技術
 基礎物理学実験
無重力環境下での精密計測
宇宙・衛星内環境のより深い理解
宇宙空間での高い安定度の実現
さまざまな応用
地球環境観測 (ADM-Aeolus, GIFTS),
基礎物理実験, マイクロ波標準, 通信
(ACES), 惑星探査 (TPF-C), X線観測
(MAXIM), フォーメーションフライト (LISA,
GRACE-follow-on)
長時間安定な無重力環境
宇宙環境利用の新しい可能性
基礎物理学実験, 材料工学
フォーメーションフライト
のための基礎技術
(TPF-C, LISA, GRACE follow-on)
小型低雑音スラスタの宇宙実証